## Slide 1: Image Acquisition and Representation
Brent M. Dingle, Ph.D. 2015
Game Design and Development Program
Mathematics, Statistics and Computer Science
University of Wisconsin - Stout
Some Details

## Slide 2: Lecture Objectives
Previously
  Image Acquisition and Generation
  Image Display and Image Perception
  HTML5 and Canvas
Today
  Brief summary of direction of study
  What is a Digital Image?

## Slide 3: What we will Study
Implicitly: Visual Perception
  Light and EM Spectrum, Image Acquisition, Sampling, Quantization
Image Compression
  General Understanding
Image Manipulation/Enhancement
  in the Spatial Domain
    noise models, noise filtering, image sharpening…
  in the Frequency Domain
    Fourier transform, filtering, restoration…
Image Analysis
  Object Identification,
  Image Recognition,
  Edge/corner detection,
  Circle/line/ellipse detection…

## Slide 4: What’s useful in this?
Reasons for Compression
  Image data needs to be accessed at different time or location
  Limited storage space and transmission bandwidth
Reasons for Manipulation
  Image data acquisition was non-ideal, transmission was corrupted, or display device is less than optimal
    reasons for restoration, enhancement, interpolation…
  Image data may contain sensitive content
    hide copyright, prevent counterfeit and forgery
Reasons for Analysis
  Reduce burden and error of human operators via automation
  Allow a computer to “see” for various AI tasks

## Slide 5: What we will Discover
Digital Image Processing connects many dots
  Linear Algebra, Matrix Theory and Statistics
  Calculus and Fourier Transforms and Wavelets
  AI, Neuroscience, and Psychology

## Slide 6: Moving On
How do we get to DOING this stuff ?
Must first understand WHAT a digital image is.

## Slide 7: What is a Digital Image?
Recall
  Digital Image Processing (DIP)
    Is computer manipulation of pictures, or images, that have been converted into numeric form
Implies a Digital Image
  Is a picture or image converted to numeric form
Let us look at what that really means…

## Slide 8: What is a Digital Image?
2D function f(x, y) or a matrix
  x, y, and f(x, y) are discrete and finite
  Image size = (xmax) by (ymax)
    e.g. 1024 x 768
  Pixel Intensity Value = f(x,y)
    bounded by 0 and 255
hmm… how does color fit in?
Think black and white for the moment
spoiler: for color think vector function

## Slide 9: Pixel Values
= 0
= 0.5
= 1
f(x, y) values

## Slide 10: How do we get the numbers?
Three principal sensor arrangements

## Slide 11: How do we get the numbers?
Three principal sensor arrangements
  Single
  Line
  and Array

## Slide 12: How do we get the numbers?
Three principal sensor arrangements
  Single
  Line
  and Array

## Slide 13: How do we get the numbers?
Three principal sensor arrangements
  Single
  Line
  and Array

## Slide 14: Single Sensor: Moving
Photodiode
  Constructed of silicon materials whose output voltage waveform is proportional to light
  Generating a 2D image using a single sensor requires relative displacements in the horizontal and vertical directions between the sensor and area to be imaged
Microdensitometers are mechanical digitizers that use a flatbed with the sensor moving in two linear directions

## Slide 15: MOVING Sensor Strips
In-line arrangement of sensors
    i.e. a strip of sensors
  Strip provides imaging elements in one direction
    i.e. x direction
  Motion perpendicular to the strip images in the other direction
    i.e. y direction
strip moves

## Slide 16: Sensor Arrays
Individual sensors are arranged in a 2D array
  Used in digital cameras
  Entire image formed at once
  No motion necessary

## Slide 17: Signals
A signal function conveys information
  1D signal: f(x) waveform
  2D signal: f(x, y) image
  3D signal: f(x, y, z) volumetric data or f(x, y, t) animation (spatiotemporal volume)
  4D f(x, y, z, t) volumetric data over time
The dimension of the signal is equal to its number of indices
In this course we focus on 2D images: f(x, y)

## Slide 18: Digital Image
Image produced as an array of picture elements (pixels) in the frame buffer
http://digitalsafari.pbworks.com/w/page/84764749/02%20Pixel%20Art

## Slide 19: Image Classification
Images can be classified by
  whether they are defined over all points in the spatial domain
  and whether their image values have finite or infinite precision
  If the position variables (x, y) are continuous then the function is defined over all points in the spatial domain
  If (x,y) is discrete then the function can be sampled at only a finite set of points (i.e. the integers)
  The value that a function returns can also be classified by its precision, independently of x and y

## Slide 20: Image Classification
Quantization refers to the mapping of real numbers onto a finite set
  a many-to-one mapping
  similar to casting a double precision to an integer

## Slide 21: Digital Image: Summary
Digital Image Processing (DIP)
    Is computer manipulation of pictures, or images, that have been converted into numeric form
A Digital Image
    Is a picture or image converted to numeric form
    In grey-scale the image can be thought of as
      2D function f(x, y) or a matrix
      x, y, and f(x, y) are discrete and finite
      Image size = (xmax) by (ymax), e.g. 1024 x 768
      Pixel Intensity Value = f(x,y)  [0, 255]

## Slide 22: Summary So Far
Digital Image Processing (DIP)
      Is computer manipulation of pictures, or images, that have been converted into numeric form Previously
A Digital Image
      Is a picture or image converted to numeric form
      In grey-scale the image can be thought of as
        2D function f(x, y) or a matrix
        x, y, and f(x, y) are discrete and finite
        Image size = (xmax) by (ymax),
        Pixel Intensity Value = f(x,y)  [0, 255]
                for color f(x,y) returns a vector
      Digitally created by various physical devices
Next
  Image Acquisition – part 2
  Image Representation

## Slide 23: Grayscale (and Color) Imaging
Image Acquisition
  Light and Electromagnetic spectrum
  Charge-Coupled Device (CCD) imaging
  Sampling and Quantization
  Bayer Filter
    a common color filter array (CFA)
Image Representation
  Spatial resolution
  Bit-depth resolution
  Local neighborhood

## Slide 24: Electromagnetic (EM) Spectrum

## Slide 25: Visible Spectrum
Visible range: 0.43µm(violet)-0.78µm(red)
Six bands:
  violet, blue, green, yellow, orange, red
The color of an object is determined by the nature of the light reflected by the object
Monochromatic light (gray level)
Three elements measuring chromatic light
  Radiance, luminance and brightness

## Slide 26: Questions so far
Questions on EM spectrum?
Image Acquisition
  Light and Electromagnetic spectrum
  Charge-Coupled Device (CCD) imaging
  Sampling and Quantization
  Bayer Filter
    a common color filter array (CFA)

## Slide 27: CCD Imaging (Sensor Array)

## Slide 28: Charged Coupled Device (CCD)
A CCD is a device for the movement of electrical charge
  usually from within the device to an area where the charge can be manipulated
    often converted into a digital value
  CHARGE into digital value
    where charge is proportional to light exposure

## Slide 29: Single Pixel of a CCD Array
The top gate is held at a positive voltage
  gate = metal electrode
Notes: Reference: http://www.hatiandskoll.com/2013/04/09/secrets-of-charge-coupled-devices-ccd/

## Slide 30: Single Pixel of a CCD Array
Below the gate Silicon Dioxide = SAND
    an insulator carrying no electrons
    keeps electrons away from gate
Notes: Reference: http://www.hatiandskoll.com/2013/04/09/secrets-of-charge-coupled-devices-ccd/

## Slide 31: Single Pixel of a CCD Array
Below the sand
N-type silicon Epitaxal layer
  photosensitive layer
  light can knock electrons off of it
Notes: Reference: http://www.hatiandskoll.com/2013/04/09/secrets-of-charge-coupled-devices-ccd/

## Slide 32: Single Pixel of a CCD Array
Below the Epitaxal layer
P-type silicon layer
  kept at negative voltage
Notes: Reference: http://www.hatiandskoll.com/2013/04/09/secrets-of-charge-coupled-devices-ccd/

## Slide 33: Single Pixel of a CCD Array
Light hits the bottom side of this
  Photoelectrons fill up the holes in the P-Type layer
    longer exposure means more holes filled up
      holes are “wells” to collect electrons
        maximum number of electrons a well can hold = well capacity
Notes: Reference: http://www.hatiandskoll.com/2013/04/09/secrets-of-charge-coupled-devices-ccd/

## Slide 34: Single Pixel of a CCD Array
End result
  Device which stores charge proportional to light exposure
  Make an array of them
Notes: Reference: http://www.hatiandskoll.com/2013/04/09/secrets-of-charge-coupled-devices-ccd/

## Slide 35: Shift To Get Readout
CCD uses programmed voltages to shift the charge between pixels
  Done by taking a pixel’s voltage to zero
    thus transferring it to adjacent pixel held at voltage V
  Shift continues until it reaches the readout point
Left Image by: Michael Schmid from Wikicommons Creative Commons License,
Right Image: David E. Wolf, http://www.hatiandskoll.com/2013/04/10/more-secrets-of-charge-coupled-devices/
Notes: Ref: http://www.hatiandskoll.com/2013/04/10/more-secrets-of-charge-coupled-devices/

## Slide 36: Shift To Get Readout
At output point
  accumulated charge acts as a voltage
  Analog to Digital (A/D) converter converts voltage to digital signal
    Image is now digitized
Left Image by: Michael Schmid from Wikicommons Creative Commons License,
Right Image: David E. Wolf, http://www.hatiandskoll.com/2013/04/10/more-secrets-of-charge-coupled-devices/
Notes: Ref: http://www.hatiandskoll.com/2013/04/10/more-secrets-of-charge-coupled-devices/

## Slide 37: Sloppy Noise
As charge moves from pixel to pixel, there is spillage
  Which is one cause of “noise” in the signal
    Noise can cause “errors” in readout/display
Image by: Michael Schmid from Wikicommons Creative Commons License,
Notes: Ref:
http://www.hatiandskoll.com/2013/04/10/more-secrets-of-charge-coupled-devices/
http://www.hatiandskoll.com/2013/04/11/building-a-digital-camera-sensor-from-a-charge-coupled-device/

## Slide 38: Device Limits: Dynamic Range
Dynamic Range of the Device
  Is the number of grey levels that a device can be divided into
    Is defined by the number of electrons
    This is controlled by the number of electrons in the well (the holes in the P-type silicon layer)
NASA public domain image of CCD sensor array

## Slide 39: Questions so far
Questions on CCD Hardware Aspects of Image Acquisition?
Image Acquisition
  Light and Electromagnetic spectrum
  Charge-Coupled Device (CCD) imaging
  Sampling and Quantization
  Bayer Filter
    a common color filter array (CFA)

## Slide 40: Adding Some Math to The Picture
Image Formation Model
  f(x,y) = i(x,y) * r(x,y) + n(x, y)
f(x, y) | 0 < f(x, y) <  | Intensity which is proportional to the energy radiated by a physical source
i(x, y) | 0 < i(x, y) <  | illumination is amount of source illumination incident on the scene being viewed
r(x, y) | 0 < r(x, y) < 1 | reflectance is the amount of illumination reflected by objects in the scene
n(x, y) |  | noise is various measurement errors
nature of i(x, y) is determined by the illumination source (light source)
nature of r(x, y) is determined by the object(s) in the scene

## Slide 41: Continuous to Discrete
f(x, y) in the “real” world is continuous
  The sensors provide a continuous voltage waveform whose amplitude and spatial behavior are related to the physical phenomenon being sensed
We must convert the continuous sensed data into digital form
  The A/D converter helps
  Lets look at some of the math behind it

## Slide 42: Sampling and Quantization
Sampling
  Digitizing the coordinate values
    this can be thought of as our “pixel” resolution
Quantization
  Digitizing the amplitude
    A/D converter does most of this for us

## Slide 43: Sampling and Quantization: 1D
Generating a digital image
(a) Continuous Image

## Slide 44: Sampling and Quantization: 1D
Generating a digital image
(a) Continuous Image
(b) A scan line from A to B
in the continuous image

## Slide 45: Sampling and Quantization: 1D
Generating a digital image
(b) A scan line from A to B
in the continuous image
(c) Sampling and Quantization

## Slide 46: Sampling and Quantization: 1D
Generating a digital image
(c) Sampling and Quantization
(d) Digital Scanline

## Slide 47: Onto 2D: Sampling and Quantization

## Slide 48: Questions so far
Questions on Sampling or Quantization?
Image Acquisition
  Light and Electromagnetic spectrum
  Charge-Coupled Device (CCD) imaging
  Sampling and Quantization
  Bayer Filter
    a common color filter array (CFA)

## Slide 49: Maxwell: Experiments in Color
How does one use black and white sensors to digitize color?
  Experiments of Colour, James Clerk Maxwell, 1855
Answer (simplified)
  Color Filter Arrays (CFAs)
    Overlay the pixels with a set of Red, Green, and Blue filters

## Slide 50: Bayer Filter
Ordering of filter overlays on pixels is important
Bayer Filter
  Is one CFA option
  Note that green has twice as many pixels
    Why?
Bayer Filter overlaid on CCD
Public domain image from WikiCommons
Notes: Bayer Filter is green biased to account for human eye’s biological bias towards green sensors

## Slide 51: Zoomed in Result
Example Image acquired with a CCD chip using Bayer Filter
  Mosaic Effect leaves something to be desired/fixed
Public Domain image from WikiCommons

## Slide 52: Mosaic Effect
Original scene
Output of a 120-pixel by 80-pixel sensor with Bayer Filter
3. Output color-coded with Bayer Filter colors
4. Reconstructed Image after interpolating missing color information

## Slide 53: Another Example
Original Scene
What the Camera Sees
Images from: http://www.cambridgeincolour.com/tutorials/camera-sensors.htm

## Slide 54: Even More Examples
Bayer Image (400%)
Image from: http://www.red.com/learn/red-101/bayer-sensor-strategy

## Slide 55: Even More Examples
Full Color Image (400%)
Image from: http://www.red.com/learn/red-101/bayer-sensor-strategy

## Slide 56: Even More Examples
Full Color Image (100%)
Image from: http://www.red.com/learn/red-101/bayer-sensor-strategy

## Slide 57: Mosaic Removal: CFA Interpolation
Bayer de-mosaicking is the process of translating a CFA (Bayer array) of primary colors into a final image that contains full color information
    Interpolation methods will be discussed in a later lecture
    The interested may check out various papers online
Paper 1: http://research.microsoft.com/en-us/um/people/lhe/papers/icassp04.demosaicing.pdf
Presentation 1: https://courses.cs.washington.edu/courses/cse467/08au/pdfs/lectures/09-Demosaicing.pdf
Paper 2: http://www.ece.ncsu.edu/imaging/Publications/2002/demosaicking-JEI-02.pdf
Paper 3: http://graphics.cs.williams.edu/papers/BayerJGT09/bayer-jgt09.pdf
Paper 4: https://hal.inria.fr/hal-00683233/PDF/AEIP_SOUMIS.pdf
Paper 5: http://research.microsoft.com/pubs/102068/Demosaicing_ICASSP04.pdf

## Slide 58: Questions so far
Questions on Bayer Filters?
  Image Acquisition
    Light and Electromagnetic spectrum
    Charge-Coupled Device (CCD) imaging
    Sampling and Quantization
    Bayer Filter
      a common color filter array (CFA)

## Slide 59: Grayscale (and Color) Imaging
Image acquisition
  Light and Electromagnetic spectrum
  Charge-Coupled Device (CCD) imaging
  Bayer Filter
    a common color filter array (CFA)
  Sampling and Quantization
Image representation
  Spatial resolution
  Bit-depth resolution
  Local neighborhood

## Slide 60: Images as Matrices
Resolution in
Spatial (x, y) coordinates
and
Bit-Depth (pixel values)

## Slide 61: Spatial Resolution: Subsampling
Reducing image size by cutting out every other row/column
… appears mostly ok, w.r.t. appearance
… BUT what if we “zoom in” or keep image size “big”

## Slide 62: Spatial Resolution: Resampling
Instead of discarding rows and columns (reducing image size) – Resample to 1024x1024
i.e. Duplicate rows and columns with what previously was “kept” (keep image size)

## Slide 63: The Message
Use caution when scaling an image
  The obvious methods may have strange effects
Public Domain Image from Wikipedia
Images from: http://www.imagemagick.org/Usage/resize/

## Slide 64: Bit-Depth Resolution

## Slide 65: Bit Depth Resolution (fewer bits)

## Slide 66: Neighborhoods
Neighbors of a pixel p=(i,j)
N4(p)={(i-1,j),(i+1,j),(i,j-1),(i,j+1)}
N8(p)={(i-1,j),(i+1,j),(i,j-1),(i,j+1),
(i-1,j-1),(i-1,j+1),(i+1,j-1),(i+1,j+1)}
Adjacency
4-adjacency: p,q are 4-adjacent if p is in the set N4(q)
8-adjacency: p,q are 8-adjacent if p is in the set N8(q)
Note that if p is in N4/8(q), then q must be also in N4/8(p)

## Slide 67: Distance Definitions
Euclidean distance
(2-norm)
D4 distance
(city-block distance)
D8 distance
(checkboard distance)
0
1
1
1
1
0
1
1
1
1
0
1
1
1
1
1
1
1
1
2
2
2
2
2
2
2
2
2
2
2
2
2
2
2
2
2
2
2
2
2
2
2
2
3
3
3
3
3
3
3
3
4
4
4
4
2
2
2
2

## Slide 68: Summary
Image acquisition
  Light and Electromagnetic spectrum
  Charge-Coupled Device (CCD) imaging
  Sampling and Quantization
  Bayer Filter
Image representation
  Spatial resolution
  Bit-depth resolution
  Local neighborhood
We understand digital images!
How and Why!

## Slide 69: Questions?
Beyond D2L
  Examples and information can be found online at:
    http://docdingle.com/teaching/cs.html
    Continue to more stuff as needed

## Slide 70: Extra Reference Stuff Follows

## Slide 71
Bryce Bayer’s 1976 patent
  Front Page
  Demonstrates his terminology of luminance and chrominance sensitive elements

## Slide 72: Credits
Much of the content derived/based on slides for use with the book:
  Digital Image Processing, Gonzalez and Woods
Some layout and presentation style derived/based on presentations by
  Donald House, Texas A&M University, 1999
  Bernd Girod, Stanford University, 2007
  Shreekanth Mandayam, Rowan University, 2009
  Igor Aizenberg, TAMUT, 2013
  Xin Li, WVU, 2014
  George Wolberg, City College of New York, 2015
  Yao Wang and Zhu Liu, NYU-Poly, 2015
  Sinisa Todorovic, Oregon State, 2015